## Slide 1: Tutorial Weld Strength Eurocode3, DNV OS-C101 and C201
14 Dec 2020
version 2020.0.2

## Slide 2: Content
This step-by-step tutorial demonstrates how to perform the weld strength check according to Eurocode 3, DNV OS-C101-LRFD, DNV OS-C201-WSD standards in SDC Verifier.
The following steps are covered:
Weld Finder Tool detailed review;
Weld Stress calculations;
Standards creation;
Report preparation and results.

## Slide 3: Open Project
www.sdcverifier.com
1
2
Launch SDC Verifier
Open the project Weld Strength check_example
2.

## Slide 4: Run Analysis
www.sdcverifier.com
4
Execute Analyze from Job1 context menu
1
1.

## Slide 5: Weld Finder – General overview
www.sdcverifier.com
1
Execute Recognition =>Weld Finder => Edit.
Move Welds. Order is important when the same element belongs to 2 welds.
Add, Edit, Combine, Split and Remove Weld(s).
Preview selected weld(s).
Plot of selected weld(s) in colors and with labels of IDs (drop-down menu).
Navigate option in order to find weld by ID.

## Slide 6: Add exception rule for recognition
Press Settings
1
Press Edit for Not weld properties.
Select property ID4.
2
3
Select property ID5.
4
Press Add.
5
1.
2.
3.
4.
Connections with properties 4 and 5 are not treated as welds
5.
6
Press
6.

## Slide 7: Not welded properties. Option2
It is possible to select properties manually in Femap by elements to add a not welded combination

## Slide 8: Recognize welds
Press Find.
1
Press Close.
2
2.
1.
3.
Press Weld Strength Settings.
3

## Slide 9: Weld Finder – Details
Edit, Combine, Split, Export and Remove Weld(s).
Preview selected weld(s).
Plot of selected weld(s) in colors and with labels of IDs (drop-down menu).
Navigate option in order to find a weld by ID.
This filter can be used to search the weld(s) due to different parameters (length, thickness, area, weld only, non weld only etc.).
Selection gives a possibility to select a part of the model (group, component) for making changes.

## Slide 10: Weld Finder – Set weld parameters
Possibility to modify or change length, thickness, coordinate system and origin to all selected weld(s) parts.
Restore default data if some of them were assigned incorrectly.
Set Welded only - change selected non-welded parts by selecting elements on the model.
Possibility to apply weld type and dimensions of weld to all selected weld(s) parts.
Set Non-welded only - change selected welded parts by selecting elements on the model.

## Slide 11: Set welded parts by elements
Select all welds part by pressing Ctrl+A keys combination.
1
Press Set welded parts by elements to find weld parts by elements and include them in weld strength calculations (also this command could be performed for few or single weld part).
2
1.
2.

## Slide 12: Set weld part type welded (manually)
In order to get refreshed plot of the weld(s), select all weld parts by using Ctrl+A keys combination and choose command Welded/non-welded parts
3.
Select Non-Welded element(s) which should be changed to Welded element(s).
1
Press OK.
Press Cancel.
2
3
It is sufficient to select only one element from a weld part to pick full part automatically.
Updated plot shown below

## Slide 13: Set weld parameters
1
Select all weld parts by pressing Ctrl+A keys combination.
2
Select the type of weld Double fillet.
3
Choose the method: Apply by throat thickness.
4
Select type (half of thickness welded plate).
1.
2.
3.
4.
5.
5
Press Apply.
6
Press OK.
6.
For beams elements t is the minimum thickness of shape. For bars element t is the minimum of height/width. For plates element t is a plate thickness.

## Slide 14: Export Welds
1
Press Export weld.
2
Select Export welds.
3
Press Export.
4
Press OK twice.
4.
2.
3.
4.

## Slide 15: Weld Stresses Calculation
Angles matrix of rotations due to weld throat plane.
Stress calculations
Top (T)
Bottom (B)
x
z
y
: weld length
Moments depend on the axis in a weld plane and are also included in the weld strength calculations
τ|| = shear design stress (in plane of the throat) parallel to the axis of the weld (equal to X direction in the check);
σ⊥= normal design stress perpendicular to the throat (equal to Y direction of the check);
τ ⊥ = shear design stress (in plane of the throat) perpendicular to the axis of the weld (equal to XY direction of the check)
The stresses , and are evaluated at the points T1, T2, B1 and B2 as follows:

## Slide 16: Implementation of weld stresses
Von Mises stress at certain point.

## Slide 17: Add Eurocode3 (EN1993-1-8)
Execute Add => Eurocode3 Weld
(EN 1993-1-8. 2005) in the Standards context menu.
1
Eurocode3 Weld (EN 1993-1-8. 2005) Design of joints is implemented to verify the structure stability of each structural member (weld).
1.

## Slide 18: Eurocode3 Correction Factor
Weld Selection gives a possibility to include or exclude weld(s), preview chosen weld(s) or go to weld finder.
1
Press the button to select the Correction factor.
2
Select the material for which the Correction factor will be applied.
3
Input value of the Correction factor according to the table 4.1, and press Apply to selected.
4
Press OK.
1.
3.
2.
4.

## Slide 19: Eurocode3 Weld Strength
1
Press the button to apply Material Yield and Tensile parameters.
2
Select the material for which the Properties will be applied.
3
Input value of the Material Yield and Tensile parameters, and press Set.
4
Press OK.
5
Press OK.
2.
3.
4.
Gamma_M2 - material resistance factor for plated structures is a constant value (=1.25) and used in calculations to check a base material strength.
5.

## Slide 20: Create extreme table
2.
5.
6.
2.
3.
4.
1
Execute Extreme Table in the Weld Check Total context menu.
2
Press the button and select Load Group 1
3
Press OK.
4
Selection: All Entities.
5
Press Fill Table.
6
Press OK.
Extreme table for ‘1..Load Group 1’ can be added to DNV OS-C101 and DNV OS-C201 standards respectively.
1.

## Slide 21: Create criteria plot
1
Execute Criteria Plot in the Weld Strength Check context menu
2
Load: Load Group 1;
Parameter: UF Overall;
Selection: All Entities.
3
Press the to preview Plot in Femap
4
Press OK.
Criteria plot for ‘1..Load Group 1’ can be added to DNV OS-C101 and DNV OS-C201 standards respectively.
1.
2.
3.
4.
2.
2.

## Slide 22: Add DNV OS-C101-LRFD
1
Execute Criteria Plot in the Weld Strength Check context menu
The offshore standard DNV OS-C101 (released in April, 2011) verifies structural stability for each structural member (weld).

## Slide 23: DNV OS-C101. Correction Factor
Weld Selection gives a possibility to include or exclude weld(s), preview chosen weld(s) or go to weld finder.
1
Press the button to select Correction factor.
2
Select the material for which the Correction factor will be applied.
3
Input value of the Correction factor according to the table, and press Apply to selected.
4
Press OK.
3.
2.
4.
5
Press OK.
1.
5.

## Slide 24: DNV OS-C101. Safety Factors
Gamma_Mw - material factor that is used for DNV OS C 101 calculation can be found in Table C1, section 9 of the standard.
Gamma_M - material resistance factor for plated structures is a constant value (=1.15) and used in calculations to check base material strength.

## Slide 25: Add DNV OS-C201 WSD
The offshore standard DNV OS-C201 (released in April, 2011) verifies structural stability for each structural member (weld)
Execute Add => DNV OS-C201 WSD Weld Strength (2011) in the Standards context menu.
1

## Slide 26: DNV OS C201. Correction Factor
Weld Selection gives a possibility to include or exclude weld(s), preview chosen weld(s) or go to weld finder.
1
Press the button to select Correction factor.
2
Select the material for which the Correction factor will be applied.
3
Input value of the Correction factor according to the table, and press Apply to selected.
4
Press OK.
3.
2.
4.
5
Press OK.
Gamma_M - material resistance factor for plated structures is a constant value (=1.15) and used in calculations to check base material strength.
1.
5.

## Slide 27: Add Governing Load
4.
5.
3.
6.
7.
9.
Post Processing => Governing Loads => Add
Result: from Check;
Standard: Eurocode 3 Weld.
1
2
3
Check: Weld Check Total.
Parameter: Uf Overall.
Load Group: Load Group 1.
4
5
6
Press in Limits Criteria => Absolute; Result < 0.5 => OK
7
Selection: All Entities.
8
Press OK.
9
1.
2.
8.
7.
7.

## Slide 28: Add Report
Execute Reports => Add => Designer - Results
1
There are 4 templates of the reports:
Empty – only first page and preface items are included;
Model Setup – description of the model data (materials, properties, components, boundary conditions) is included;
Results – for each load extreme displacement tables, stress and displacement plots are included. Predefined tables: sum of reaction forces, stresses/displacements summary tables. In addition all standards are included with a set of tables/plots created in the project;
Full – Model Setup + Results + all tables/plots created in jobs.
1.

## Slide 29: Report - Governing Load
2.
Select Governing Loads(LG1) => OK
Include Plot: Yes.
Show only welds: Yes.
2
3
Add Governing Load for ‘1..Load Group 1’ also possible for DNV OS-C101 and DNV OS-C201 standards.
Post Processing => Governing Loads => Import
1
1.
1.
1.
3.
2.

## Slide 30: Report - First Page
Right click on First Page => Edit.
Fill in information about project.
1
2
Select Image From View and pick.
3
Press OK.
4
Press button to generate report.
5
3.
4.
5.
1.

## Slide 31: Report - Results
Eurocode3
DNV OS-C101
DNV OS-C201