## Slide 1: Tutorial Plate Buckling DNV
20.10.2017
version 4.7

## Slide 2: Content
In this tutorial an DNV 2010 Plate Buckling Check is reviewed in details.
A part of a plate model of the ship has been used as a start FEM model.
Individual Loads, Load Sets and Load Group (Envelope) are created.
Recognition of plates using Panel Finder.
Plate Buckling tables and plots.
Reporting: preparing and generating the final report.

## Slide 3: Open Project
Launch SDC Verifier
Open project Plate_Buckling_DNV from the directory Tutorials/ Plate_Buckling_DNV.
1
2
2.

## Slide 4: Individual Loads
2.
4.
3.
1.
Click on Individual Loads.
1
Select 5 FEM Loads:
Gravity;
Ballast + crane inside;
Ballast + crane outside;
Hydroload outside;
Hydroload inside.
2
Press Create to create 5 Individual Loads.
4
Press on toolbar and “Analyze active job: 1..Job 1”
5

## Slide 5: Load Sets
www.sdcverifier.com
5
Right click on Load Sets => Create multiple.
Select highlighted cells in the table like shown on the picture and press Set to define Factors of Load Sets.(By default LS Factor is 1)
1
2
3
Load Sets are created with default titles “Load Set #”. It is possible to rename them by double-click on the respective load set title.
Alternatively, the titles and factors can be pasted from the Clipboard using Paste button.
Press OK
4
Fill in “4” into Count and press to add four Load Sets.
1.
2.
3.
4.

## Slide 6
Click on Load Groups.
Press to select all
Load Sets.
Title: Envelope
1
2
3
Press Create
4
Load Sets and Load Groups are analyzed by SDC Verifier.
1.
2.
3.
4.
Load Groups

## Slide 7: Panel Finder. Recognize Sections
Launch Panel Finder
Press Find All.
Select Sections Custom
Select all the sections and press
All sections were recognized and plates were analyzed automatically on the model.
1
2
3
4
1.
2.
3.
Custom sections are automatically recognized on the elements that do not belong to any other section (X, Y or Z) and grouped by the common edges. All the incline or curved (e.g. hull parts) sections belong to custom sections.
4.

## Slide 8: Panel Finder. Custom Section
Example: Recognized plates in colors of the hull of the full ship.
1.
2.
4.
3.
Press import from groups
Select group ‘2..Hull Part’
Press Find Plates
1
2
3
Press plot all plates with labels of IDs
4

## Slide 9: Plate Dimensions and Thicknesses
Dimensions: the results depend on plate dimensions and direction and it is important to understand how Panel Finder performs recognition. Length is considered the longest edge of plate and Width the longest perpendicular to the longest edge:
Plate Thickness: the calculations are performed on every element and thickness is taken directly from each element. It is possible to set thickness manually for a plate, in this case, the element thickness will be ignored and the user defined thickness will be used.
Example: Plate with 2 properties 0.01 and 0.02 thicknesses. Left picture displays the property labels with property thicknesses and right presents the plate buckling plot of thickness parameter:

## Slide 10: Editing plates manually
To modify plates select them from the list and press Set dimensions. It is possible to edit one parameter (Length / Width / Thickness) or few at once.
If thickness is changed, you can see in table what was the original thickness recognized from the model:
Usually, the plate directions should not be modified. But in case it is required, press Set Direction.
Free Edges should be fixed by remeshing the model and run recognition of the plates. (In tutorial we skipped remeshing, but for commercial project it is crucial step to do).
Incorrect plate dimensions/direction, plates with undefined dimensions and as result incorrect buckling factor – possible consequences of the free edges.

## Slide 11: Panel Finder. Plates Plot
1.
2.
3.
4.
length
width
Press Plot Plates tab.
Select Section X3.
Pick Colors + Labels with plates IDs.
1
2
3
Click on Plot.
4

## Slide 12: Panel Finder. Plot Options
Plate Plot can be displayed with different labels (plate id, plate dimensions or plate number of edges). Also, it is possible to show plates in colors (no labels), length and width in colors (no labels).
Plate IDs
Plate dimensions
Plate # of edges

## Slide 13: Panel Finder. Update Plates
In some cases (e.g. stiffener is not modeled) a plate is recognized not correctly, dimensions are bigger than in reality which leads to incorrect results. The plate has to be updated manually. In Section X3 plate with Id = 77 should be split in 2 plates.
If plates were modified manually and later user decided to run recognition of plates, Panel Finder will ask what to do with the modified plates:
Keep plates that was modified;
Clear everything and recognize from scratch;

## Slide 14: Panel Finder. Split Plate
4
The plate 77 is replaced with the Plates 125 and 126.
Dimensions and directions are updated automatically.
1.
2.
3.
Select Section X 3 (X = 73.36).
Select Plate 77.
Press Split selected plates by elements
1
2
3
Selected plate is displayed. Select elements for one plate and press OK.
4

## Slide 15: Panel Finder. Export Plates
4.
2.
3.
1.
Select Export Plates tab.
All Sections X: ON.
Pick Export by section.
1
2
3
Click Export.
4
5 Groups will be created for 5 Sections .
5
5.

## Slide 16: Panel Finder. Filter
Select All plates from sections
1
Filter: Undefined dimensions
2
Press Apply.
3
Table with plates is empty means that there are no plates with undefined dimensions. Press Close.
4
It is very important to check that all plates dimensions were recognized. If in the model, there are coincident nodes, coincident elements or free edges Panel Finder cannot recognize plate dimensions.
2.
3.
4.
5.
It is also possible to filter plates by shape (triangle, rectangular) or number of edges parameters.
E.g. Plates with numbers of edges > 4 can be displayed.
The filter can be applied to all Sections from X/Y/Z/Custom category or to single selected Section (option Plates of selected section)
Click on Filter tab
5
1.

## Slide 17: Add Plate Buckling DNV 2010 standard
Materials with Yield Stress = 0 shows how many materials have the yield equal to 0. If value is > 0 press to define yield.
Thickness factor gives a possibility to increase / decrease all plates thicknesses without reanalyzing the model. E.g. 1.2 means increasing thickness on 20% and decreasing stresses
By default all sections will be checked. Click to modify.
Plate Buckling transforms stresses automatically into plate direction.
The options about element stresses and plate stresses are described in the next slide
1.
2.
3.
4.
In Standards Context menu execute Add => Plate Buckling DNV RP-C-201 2010.
Resulting Material Factor = 1.15
Use Plate Average Stress: On
1
2
3
Press OK.
4

## Slide 18: Plate Buckling Stresses

## Slide 19: Views
Repeat Steps 1-4 2 times to create a view for Longitudinals (plane ZX) and Decks (plane XY)
Press Get and OK.
1.
2.
4.
To make nice a plot Views should be created firstly (the set of settings how to display a plot).
Orient model in Simcenter as shown on picture below (ZY plane)
Title: Frames
Edges: Feature
Legend Position: Right
4.
3.
2.
2.
1
2
Execute Views => Add
3
4

## Slide 20: Plate Buckling Plot
Execute Criteria Plot from Plate Buckling check context menu
Press and select Load Group “Envelope”
View: Frames
Select Section X3.
2.
3.
4.
Parameter is automatically set to Buckling Factor Overall.
5.
Press
1.
1
2
3
4
5

## Slide 21: Plate Buckling Table
Execute Expand Table from the Plate Buckling check context menu
Use Show plates results for detailed table with results for all plates. Otherwise only the worst results over Sections will be shown.
3.
2.
4.
1.
Plate with ID = 70 has the highest result in Section X 1
Section ID = 3 / Plate ID = 92
worst result among sections
All results (dimensions, stresses) are from the plate which causes
higher BF = 0.47 because Search Type = Related to Last Parameter
Press and select Load Group “Envelope”
Press Fill Table.
Show plates results: OFF
1
2
3
4

## Slide 22: Report. Tables
1.
2.
3.
4.
6.
5.
7.
4.
Execute Reports => Add Report Designer => Results.
Plate Buckling check context menu in model tree => Expand/Extreme Tables.
Press and select LS; LG loads.
Type: Expand
1
2
3
4
Select All selected sections as one selection and select all
X Sections.
6
Press OK
5
Press OK
7

## Slide 23: Report. Plots
4.
Repeat steps 1-5 for Sections Y with Longitudinals View and Sections Z with Decks View
1.
2.
5.
6.
3.
4.
4.
Click Criteria Plot in Plate Buckling check context menu
1
Parameter: Buckling Factor Overall.
2
Views: Frames
3
Press , select LS; LG Loads and Press OK.
4
Select Each selected section as separate selection and select all
X sections.
5
Press OK.
6

## Slide 24: Report. Sort tables and plots by Load
All tables and plots are sorted by loads. It is possible to sort it By Parameter; By Selection; By section as well.
1.
2.
Right click on Plate Buckling check => Sort Tables/Plots and put in chapters.
1
Sorting method => By Load.
2

## Slide 25: Report. First Page
1.
4.
3.
Right click on First Page => Edit.
Fill in information about project.
Select Image From View and pick ‘2..Frames’.
1
2
3
Press OK.
4

## Slide 26: Report
Press to generate complete report.
Press to export to Word.