## Slide 1: Tutorial F.E.M. 1.001 and Eurocode3 Fatigue
01.11.2017 version 4.7

## Slide 2: Content
This step-by-step tutorial demonstrates how to perform the fatigue check according F.E.M. 1.001 and Eurocode3 standards.
FEM 1.001 Fatigue detailed review and implementation in SDC Verifier;
Weld Recognition;
Weld Classification and Element Class;
Fatigue Results;
Eurocode3 overview;
Stress History;
Comparison of FEM 1.001 and Eurocode3 results
www.sdcverifier.com

## Slide 3
Allowable Stress Design method
www.sdcverifier.com
Fatigue F.E.M. 1.001

## Slide 4
Kappa Factor
Allowable Stress
Utilization Factor Combined
www.sdcverifier.com
Fatigue in SDC Verifier

## Slide 5
Corresponding values of Stress fatigue in SDC Verifier:
Stress Fatigue is used in Fatigue Allowable Stress calculations.
Stress Fatigue depends on:
Weld Type (W0-W2, K0-K4);
Element Group / Loading Group (B1-B6);
Material Type ( St360/St37, St510/St52).
www.sdcverifier.com
Stress Fatigue

## Slide 6
Weld Type – also called Notch Case, defines which elements belong to what weld type (K0-K4 – joints affected by welding, W0-W2 – elements and joints, not affected by welding). Weld Type depends on shape, structural design, whole pattern or type and quality of welds.
www.sdcverifier.com
Weld Type

## Slide 7
Load Spectrum
Element Group
Element Group also called Loading Group depends on: Class of Utilization, Load Spectrum.
Load Cycles | Number | Total
Moves per hour | 30 | 
Hours per day | 10 | 300
Days per year | 300 | 90000
Number of Years | 20 | 1800000
Total | Million: | 1.8
Example of Load Cycles:
Class of Utilization B7 (1.8 million < 2 x 10^6)
www.sdcverifier.com
Element Group

## Slide 8
www.sdcverifier.com
Open the starter model
Launch SDC Verifier
Execute File - Open Project.
Project: Fatigue.simv
1
2
3

## Slide 9
www.sdcverifier.com
Analyze Job
Execute Analyze from Job1 context menu
1
1.

## Slide 10
1
Execute Recognition =>Weld Finder => Edit…
2
Press Find Welds.
Press Export
3
Selection - Part of the model where to find welds
Move Welds. Order is important when one element belongs to 2 welds.
Add, Edit, Combine and Remove Welds.
Export selected welds to component. Move welds
Colored plots with Ids. Preview features
Not welded prop. – selection of the properties, which are definitely not welded.
www.sdcverifier.com
Weld Finder
1.

## Slide 11
It is possible to export weld intersections into component (Nodal or Elemental)
All welds as one component ON
All welds as one group ON
Press OK.
4
5
Simcenter group and new component will be created.
www.sdcverifier.com
Export Welds

## Slide 12
Stresses for weld elements are automatically transformed in the direction of the corresponding weld from Weld Finder Tool using the wedge method. Stresses are transformed only for plate type elements.
– angle between the element and weld x directions.
www.sdcverifier.com
Stress Transformation

## Slide 13
www.sdcverifier.com
1.
Execute Standards => Add => F.E.M 1.001 from context menu
1
Press to edit material properties.
2
3.
4.
Add FEM 1.001
2.
Amount of materials with not defined Tensile or Yield are displayed in the field
3
Tensile Strength: 360e6
Yield Stress: 240e6 and Press Set.
Press OK.
4

## Slide 14
www.sdcverifier.com
Weld Type examples

## Slide 15: Welt Type – stress direction
www.sdcverifier.com
 | Perpendicular to weld | Parallel with weld | Shear
Weld | K1 | K2 | K0
No weld | W0 |  | tD(-1) = sD(-1) / sqrt(3)
Steel Grade | σD(-1) for k=-1 elemеnt group 5 St 52-3 |  |  |  |  |  |  | 
Notch group | W0 | W1 | W2 | K0 | K1 | K2 | K3 | K4
Stress amplitude | 163.8 | 130.3 | 104.2 | 118.8 | 106.1 | 89.1 | 63.6 | 38.2

## Slide 16
4.
1
Press Define for the Weld Type.
2
3
Press to Add Condition.
Select Multiple Conditions options
4
Press Add all Welds
5
www.sdcverifier.com
Press X/Y/XY
6
X: K1 Y: K2 XY: K0
2.
5.
6.
3.
Weld Type Classification

## Slide 17
At intersecting welds all stresses are perpendicular to the weld direction.
The last condition overwrites the previous ones and settings in condition 2 => K1(X) are replaced with K2(X) for intersections
www.sdcverifier.com
1.
2.
3.
4.
1
Click All welds intersections
2
3
Press to Add Condition.
Directions: X
4
Value: K2
5
Press OK
Weld Type for weld intersections

## Slide 18
www.sdcverifier.com
1
Direction: X. Press Plot
2
Direction: Y. Press Plot
3
Press OK
1.
1, 2.
2.
Classification Plot

## Slide 19
1
Press Define for the Element Group.
2
Element Group: E6.
3
Press Apply.
www.sdcverifier.com
3
Press OK.
2.
3.
4.
1.
Element Group classification

## Slide 20
Material Type defines which steel is used: St37 or St52. Stress Fatigue values are different for different materials.
1
Press Define for the Material Type.
2
Material Type: Fe360 (Fe 37).
3
Press Apply
Press OK
4
www.sdcverifier.com
1.
2.
3.
4.
Material Type classification

## Slide 21
Table Type: Parameter over Directions.
3
Press Fill Table.
6
Press OK.
5
Parameter: Utilization Factor.
4
Execute Extreme Table in Fatigue Check context menu.
Load Group: 1..L1-L4.
1
2
www.sdcverifier.com
Utilization Factor extreme values
1.
2.
3.
4.
5.
6.

## Slide 22
1.
1
Click and select all properties
2
Press Fill Table.
4
Press OK.
3
Execute Components Table in Fatigue Check context menu.
www.sdcverifier.com
Utilization Factor over properties
2.
3.
4.

## Slide 23: Create criteria plot
Point of interest = AbsMax Total is absolute maximum utilization factors among all point of interest.
Execute Criteria Plot in Fatigue Check context menu
Parameter: Utilization Factor
1
2
3
Direction: Overall
4
Point of interest: Total Type: AbsMax
5
Press to preview Plot
6
Press OK
www.sdcverifier.com
2.
3.
4.
5.
6.

## Slide 24
A better fatigue damage can be made if load cycles are specified more accurately.
Instead of 2 million load cycles from start to end:
L1
L2
L3
L4
Load cycle | Number of cycles | Content
L4-L1 | 0,5 e6 | LS4, LS3, LS2, LS1, IL1
L4-L2 | 1,0 e6 | LS4, LS3, LS2, IL1
L4-L3 | 0,5 e6 | LS4, LS3, IL1
NB gravity load is also included because the stress variation determines the fatigue damage
www.sdcverifier.com
Eurocode3 Stress history

## Slide 25
Total number of load cycles is calculated automatically
www.sdcverifier.com
Select Fatigue Groups in Navigation tree
Title: Detailed load cycles pattern
1
2
3
Select all groups and press
4
Select 1..L1-L4 and 3..L2-L4
5
Fatigue Item Cycles: 0.5e+6 and Set.
6
Set 1e+6 cycles for 2..L3-L4
7
Press Create
1.
Add Fatigue Group (stress history)
2.
3.
5.
6.
7.

## Slide 26
www.sdcverifier.com
Add Eurocode3 Fatigue
Execute Standards => Add => Eurocode3 Fatigue
1
Consequence of Failure: Low
2
3
Assessment Method: Damage tolerant
1.
Safety Factor | Low consequence | High consequence
Damage tolerant | 1.0 | 1.15
Safe life | 1.15 | 1.35

## Slide 27: FAT classes Eurocode3
www.sdcverifier.com
 | Perpendicular to weld | Parallel with weld | Shear
Weld | 80 | 100 | 80
No weld | 160 |  | 100
For determination of FAT classes check standard!
In this tutorial only examples are given

## Slide 28: Eurocode3 Fat Class
www.sdcverifier.com
1
Press Define for the FAT Class.
2
3
Full Model: 160
For welds: X: 100; Y/XY: 80
4
All Entities: 100 (No weld)
5
For welds intersections: X: 80
2.
5.
3.
4.

## Slide 29: Classification Plot
www.sdcverifier.com
1
Direction: X. Press Plot
2
Direction: Y. Press Plot
3
Press OK
1.
1, 2.
2.

## Slide 30: Fatigue Damage Plot
www.sdcverifier.com
Execute Criteria Plot in Fatigue Check context menu
Parameter: Summed Damage
1
2
3
Direction: Overall
4
Point of interest: Total Type: AbsMax
5
Press to preview Plot
6
Press OK
2.
3.
4.
5.
6.

## Slide 31: Comparison
Eurocode 3 utilization factor at 2 million cycles
FEM 1.001 utilization factor
www.sdcverifier.com