## Slide 1: Joint Check
August 14th, 2024
SDC Verifier 2024 R1.1
ANSYS Workbench 2023 R1

## Slide 2: Content
SDC Verifier is a powerful extension to Ansys Mechanical with an advanced calculation core for checking structures according to different standards and report generation.
The goal of SDC Verifier is to automate all possible routine work and speed up a verification of the engineering projects significantly.
In this tutorial, Joint Check is reviewed in details.
General Info;
Connection Types;
Connection design;
Joint Checks according to standards;
Create Plots and Tables;
Criteria Plot comparison of Joint Checks;
The functionality of SDC Verifier Report Designer can be checked via the link to a separate tutorial (Slide 37).

## Slide 3: Launch SDC Verifier
In Ansys Workbench open JointCheck.wbpz
1
2
Execute right click on Model and select Edit
2
2

## Slide 4: Predefined Project
This tutorial uses project with predefined boundary conditions. The model contains only circular tube beams

## Slide 5: Analyze Job
1
2
Go to Home section on the Ribbon
Press on the toolbar to analyze Job
1
2
Job 1 analysis started and finished.

## Slide 6: General Info about Joint Check
Joint Check is an offshore check that verifies strength of tubular structure under tension or compression members according to the standards.
Joint is a node where two or more incline elements are connected.
Connection is a set of elements of the same plane around a joint node.
Chord is a set of non-welded elements that form straight line.
Brace is a welded to a chord element.
Joint check is based on the connections.
Each connection is a set of elements near joint node. Connections consists of Chord and braces. Brace contains only 1 element with ID defined in brackets (#). Connection can contain braces from both sides of the chord.
The information is displayed in the second brackets: U- upper braces; L- lower braces.

## Slide 7: Connection Types
2D Connection. Set of elements of one plane
3D Connection. It will be split on 2D Connections
Connection can include only circular tube shape elements. Otherwise, connection will not be recognized. Example of unrecognized connection:

## Slide 8: Add Joint Check API LRDF (1st, 1993)
1
Execute right click on Standards and select Add => Custom
3
Joint Check API LRFD is a part of the standard
API RP 2A-LRFD (1st, Jul 1993). This is the reason why the first step was to create Custom Standard.
2
Title: Joint Check;
Press OK
3
In 1..Joint Check, execute right click on Checks (0) => Add => Joint Check API LRFD (1st, 1993)
1
1
2
2

## Slide 9: Joint Check Settings
Joint Check Settings are common for all available types of joint checks: API, ISO and Norsok.
1
Press Find Connections
Joint nodes to be checked. Part of the model can be checked by selecting the required joints.
1
Maximum distance between joint nodes of one connection. Include connections that are formed by multiple joints. The recommended distance is D/4. It is possible to set custom distance.
Chord maximum curvature angle defines the maximum allowable straightness of the chord. Default angle is 3 degrees.
Angle between braces treated as in one plane. Braces that are located in different planes of one connection with an angle A to each other will be treat as in-plane connection.
Calculate all braces as TY.
Ignore all loading conditions and set all brace types to TY if turned on.
Forces tolerancee is maximum allowable difference between axial tension and compression forces that are perpendicular to the chord from one side of the connection. If forces are balanced, all braces are considered to be K joints.

## Slide 10: Check Connections Design
1
2
Select 150..Connection 150;
Press
Press Preview Connection
3
Press to remove all conditions in Chord and Braces selections
Two separate connections will be created automatically for cross type of joint with equal dimensions. With chord parallel and perpendicular.
A list of connections that are recommended to be checked.
All connections in the list are recommended to be checked as all elements of each connection are of the same diameters and thicknesses. Depending on the welding process, it is possible to modify connection and set chord and braces manually.
1
2
3
3
1

## Slide 11: Add Chord Elements
1
2
3
To add entities with Ansys Mechanical, press and select Elements by Text
Press OK
1
4
Operation: Add;
Type: Elements
Insert Mesh Elements Ids 2081, 2031
2
3
4

## Slide 12: Add Chord Elements
1
2
3
To add entities with Ansys Mechanical, press and select Elements by Text
Press OK
1
4
Operation: Add;
Type: Elements
Insert Mesh Elements Ids 2059, 1984, 1985, 2019
2
3
4

## Slide 13: Connections Design
Press Calculate
1
2
3
1
2
3
Press OK
Press OK
4
Press Close
4

## Slide 14: Connections Design
When Chord is formed by elements with different properties around the joint node and D1<>D2, D = min(D1, D2); T = min(T1, T2) are considered for calculations.
D1 = D2, D1 < D3. For such case, D3 is recognized as chord as it has bigger diameter. Naturally, pipe of bigger diameter cannot be welded to smaller. Such connections are recommended to be checked.
D1 = D2 = D3 = D4; T1 = T2 = T3; T4 > T1;
When all diameters of the connection are equal, thicknesses are compared. Element with thickness = T4 is recognized as a chord.
In both cases, such types of connections are recommended to be checked.
In case when :
D1 = D2 = D3 = D4;
T1 = T2 = T3 = T4;
When all diameters of connection are equal,
Thicknesses are compared. Element with thickness = T4 is recognized as chord.

## Slide 15: Joint Check API LRFD Overview
Selection and recognition settings
Navigation. Fill Connection ID and Press
Navigate to find a connection in the table
Connection info. Chord, Braces, and their properties
Add, Edit, Preview and Remove selected connections
#401,410 – IDs of related elements in the model.
(U) – Upper (0°-180°) braces (L) – Lower (180°-360°) braces

## Slide 16: Joint Check API LRFD Display of Connections
Select all connections in the list (Ctrl + A)
1
2
Press to display all connections with labels of IDs
1
2

## Slide 17: Set Overlapped Braces and Resistance Coef.
1
2
Select Connection 52 and press to edit it
Press Set Braces Overlapping
The resistance coefficient depends on the strength of the welding and is used in calculations of overlapping (Section E.3.2 API 2A RP LRFD). Table J 2.5 is taken from the Load and resistance factor design specification for structural steel buildings on December 27, 1999 (AISC). The default value is 0.9. It can be applied to overlapped braces.
1
1
2

## Slide 18: Set Overlapped Braces and Resistance Coef. (Continuation)
3
Press Set Overlapped (Yes) to relevant Braces
4
Press Close
5
Press OK
Alternatively, coefficients to multiple connections can be set by pressing Set Resistance Coefficients button in Joint Check window.
3
4
5

## Slide 19: Brace Load Transfer Functionality
Load transfer has an influence on a chord stability. Axial branch capacity is calculated using Can and Nominal chord element parameters (Section E.3.4 API 2A RP LRFD)
Effective length is calculated for each brace separately. It is the minimum distance from the end of the can till the point of intersection of chord and brace multiplied by 2. L1, L2 <=1.25D. If L1 and L2 exceed 1.25D distance, can will not be recognized.
Tc ≥ T nominal.
L = 2 * L1 = 0.6293 – effective length for the left brace
L = 2 * L3 = 2 * L4 = 1 – effective length for the middle brace
L = 2 * L2 = 0.6293 – effective length for the right brace T nominal = 0.01; Tc = 0.02;
It is possible to set load transfer and effective length manually by pressing Set brace load transfer button.
1
Press OK
1

## Slide 20: Material Properties
All results are based on material fatigue parameters Tensile Strength and Yield Stress. Parameters are used to define the allowable static stress of the material. Allowable = Min(Yield Stress, Tensile Strength * 2 / 3). For ISO and Norsok joint checks:
Allowable = Min(Yield Stress, Tensile Strength * 0.8).
Alternatively, it is possible to set values for selected materials in the Main Window. Select material, fill parameters and press Apply.
1
In Model section, execute right click on Materials (1) and select Edit Multiple
2
Set required properties and press OK
1
2

## Slide 21: Brace Joint Type
Joint type is based on type of loading. By checking if forces of connection are balanced joint types are classified on K, TY and X (Cross).
K – tension and compression loads are balanced.
TY – tension or compression load goes as shear force in a chord.
X (Cross) – Connection has to contain braces from the both sides to check on cross joint. If balanced forces of all braces of one side and balanced forces of all braces of other side are equal, all braces are classified as X (Cross).
Interpolation – the order of joint type recognition is the following: K -> X (Cross) -> TY. Each brace can have all 3 types of joint type taken as percentage of axial load of brace to summation of all braces loads.
Projected – axial force that is perpendicular to the chord.
If Projected = 0 – brace type is set to TY.
If percentage is not mentioned, 100% is taken for the type.

## Slide 22: Gaps
Gap is the distance between two differently loaded braces (tension and compression) on a shell of a chord.
Depending on load, it is possible that brace can have two or more gaps to considerate. Each gap percentage depends on the percentage of a taken load:
Projected – axial force of the brace, perpendicular to the chord;
FTension – sum of all positive projected axial forces;
FCompression – sum of all negative projected forces;
𝑝𝑒𝑟𝑐𝑒𝑘𝑡𝑎𝑔𝑒 =
𝐹𝐶𝑜𝑚𝑝𝑟𝑒𝑠𝑠𝑖𝑜𝑘
𝑝𝑟𝑜j𝑒𝑐𝑡𝑒𝑑
𝐹𝑇𝑒𝑘𝑠𝑖𝑜𝑘
, 𝑝𝑟𝑜j𝑒𝑐𝑡𝑒𝑑 < 0
, 𝑝𝑟𝑜j𝑒𝑐𝑡𝑒𝑑 ≥ 0
𝑝𝑟𝑜j𝑒𝑐𝑡𝑒𝑑

## Slide 23: Joint Check Expand Table
In Standards => 1..Joint Check => Checks (1), execute right click on 1..Joint Check 1 and select Table (expand/extreme)
1
2
3
4
5
Press and select Load Set => Load Set => 1..All loads combination;
Press OK
Filter by Parameter: Overall Utilization Factor
Sort by Parameter: Overall Utilization Factor
Press Fill Table
Press OK
Plot Forces – plot original, transformed axial forces and brace joint types;
Plot Gaps – plot gaps if there is more than one brace in connection;
Plot Classification – plot brace joint types;
4
2
Table build type allows to fill parameters in Columns and connections in Rows and vice versa. Parameters in Rows can be used for a single connection, for example.
1
2
2
3
2
5

## Slide 24: Joint Check Expand Flow Table
In Standards => 1..Joint Check => Checks (1), execute right click on 1..Joint Check 1 and select Flow Table (over loads)
1
2
3
4
In Loads Count, press and select All Loads
Press Fill Table
Press OK
3
4
1
2
Skip rows without maximum refers to the single connection. If load does not cause extreme values on any parameter it will not be displayed.
It is possible to display only Load Results, only Min/Max results or both.
Expand Flow table is used to display multiple load results at once for each selected connection.
2

## Slide 25: Joint Check Criteria Plot
1
2
3
4
Press and select Load Set => Load Set => 1..All loads combination;
Press OK
Parameter: Overall Utilization Factor
Press and then Preview
In Standards => 1..Joint Check => Checks (1), execute right click on 1..Joint Check 1 and select Criteria Plot
5
Press OK
1
2
2
2
5
4
4
2
3

## Slide 26: Add Joint Check API WSD (21st, 2000)
1
In 1..Joint Check, execute right click on Checks (1) => Add => Joint Check API WSD (21st, 2000)
1
Joint Check API WSD is a part of the Standard API RP WSD (21st, published in 2000).
Joint Check API WSD interface is similar to Joint Check API LRFD.

## Slide 27: Find connections in Joint Check API WSD 2
1
2
3
Press Find Connections
Press Close
Press OK
The detailed descriptive steps on how to check Connections Design have been presented on slides 10-19.
1
2
3

## Slide 28: Joint Check API WSD 2 Criteria Plot
1
2
3
4
Press and select Load Set => Load Set => 1..All loads combination;
Press OK
Parameter: Overall UF
Press and then Preview
In Standards => 1..Joint Check => Checks (2), execute right click on 2..Joint Check API WSD 2 and select Criteria Plot
5
Press OK
2
2
5
4
2
3
1
2
Steps on how to add Table (expand/extreme) and Flow Table (over loads) are described in slides 23 and 25.
4

## Slide 29: Add Joint Check ISO (1st, 2007)
1
In 1..Joint Check, execute right click on Checks (2) => Add => Joint Check ISO (1st, 2007)
1
Joint Check ISO is a part of the Standard ISO 19902 (first edition, published 12 DEC 2007).
Joint Check ISO interface is similar to Joint Check API.

## Slide 30: Find connections in Joint Check ISO 3
1
2
3
Press Find Connections
Press Close
Press OK
The detailed descriptive steps on how to check Connections Design have been presented on slides 10-19.
1
2
3

## Slide 31: Joint Check ISO 3 Criteria Plot
1
2
3
4
Press and select Load Set => Load Set => 1..All loads combination;
Press OK
Parameter: Overall Utilization Factor
Press and then Preview
In Standards => 1..Joint Check => Checks (3), execute right click on 2..Joint Check ISO 3 and select Criteria Plot
5
Press OK
2
2
5
4
2
3
1
2
Steps on how to add Table (expand/extreme) and Flow Table (over loads) are described in slides 23 and 25.
4

## Slide 32: Add Joint Check Norsok (Rev.3, 2013)
1
In 1..Joint Check, execute right click on Checks (3) => Add => Joint Check Norsok (Rev.3, 2013)
1
Joint Check Norsok is a part of the Standard Norsok N004 (Rev.3, February 2013).
Joint Check Norsok interface is similar to Joint Check API.

## Slide 33: Find connections in Joint Check Norsok 4
1
2
3
Press Find Connections
Press Close
Press OK
The detailed descriptive steps on how to check Connections Design have been presented on slides 10-19.
1
2
3

## Slide 34: Joint Check Norsok 4 Criteria Plot
1
2
3
4
Press and select Load Set => Load Set => 1..All loads combination;
Press OK
Parameter: Overall Utilization Factor
Press and then Preview
In Standards => 1..Joint Check => Checks (4), execute right click on 2..Joint Check Norsok 4 and select Criteria Plot
5
Press OK
2
2
5
4
2
3
1
2
Steps on how to add Table (expand/extreme) and Flow Table (over loads) are described in slides 23 and 25.
4

## Slide 35: Criteria Plot Comparison of Joint Checks
Joint Check 1
Joint Check API WSD 2

## Slide 36: Criteria Plot Comparison of Joint Checks (Continuation)
Joint Check Norsok 4
Joint Check ISO 3

## Slide 37: Create Reports in Report Designer
To learn how to obtain reports, please check a separate Tutorial that depicts the functionality of SDC Verifier Report Designer. It may be downloaded via this link:
https://sdcverifier.com/tutorials/report-designer/